## Slide 1
HELIOS POSTPROCESS STATUS
PDD Wetted-Foam Calibration
& HDD WT_cthomas Reference Match
Prof. T. Mehlhorn
University of Michigan
Prepared for review meeting with W. Trickey, Xcimer Energy · June 3, 2026

## Slide 2
WHAT WE'LL COVER
Agenda
01
PDD wetted-foam calibration
fab007 production point, foam→ice isolation, kernel verification, 1D ray-trace limits
02
PDD design study & recommended anchors
Two-plateau yield staircase (FL=0.012 + geometric defocus); c33_burn / c25_burn
03
HDD WT_cthomas → Thomas Vulcan reference
Three calibration knobs, picket-vs-FL isolation, production anchor picket_012
04
RHINO cross-validation + adiabat convention story
Same .exo match to 0.1% in matching convention; fully_ionized_dt vs partially_ionized
05
Tooling improvements + next steps for discussion
7 new RHINO diagnostics, convention-aware comparison; questions for Cliff
Mehlhorn → Trickey · Helios postprocess review · June 3 2026
2

## Slide 3
PART 1 · POLAR DIRECT DRIVE
PDD setup: Olson 2021 wetted-foam target
Target & drive
Olson 2021 PDD wetted DT-CH foam capsule
Drive: NIF PDD; 2.15 MJ; 4-ring fixed-pointing
Helios 1D spherical ray-trace; foot 25 TW, peak 329 TW
Production point: fab007 (foot25_s018_c37_burn)
Production geometry
Cone half-angle | 37°
Spot radius | 0.18 cm (Gaussian)
Focus position | 0.22 cm (≈ R_initial)
Flux limiter f_prism | 0.007 (knee of FL curve)
α deposition | Non-local transport
LILAC reference (Olson 2021)
Yield | 87.4 MJ
Adiabat α (mass-avg) | 3.0
V_impl | 410 km/s
⟨T_hs⟩ (n-avg) | 22.5 keV
⟨P_hs⟩ | 193 Gbar
HS ρR (T>4.5 keV) | 0.85 g/cm²
Goal
Reproduce LILAC kinematics AND yield with a defensible Helios calibration; identify what knobs (geometry, FL, EOS) close the gap; rule out Helios algorithm bugs.
Mehlhorn → Trickey · Helios postprocess review · June 3 2026
3

## Slide 4
PART 1 · POLAR DIRECT DRIVE
Drive-phase calibration matches; yield deficit is real
Metric | fab007 | LILAC | Δ | 
Peak velocity | 421 km/s | 410 km/s | +2.7% | ✓ matches
Peak ρR | 1.01 g/cm² | 1.05 g/cm² | −3.6% | ✓ matches
⟨T_hs⟩ | 23.1 keV | 22.5 keV | +2.7% | ✓ matches
⟨P_hs⟩ | 206 Gbar | 193 Gbar | +6.6% | ✓ matches
Hot-spot ρR (T>4.5 keV) | 0.35 g/cm² | 0.85 g/cm² | −58% | ← cause
Yield | 26 MJ | 87 MJ | −70% | ← deficit
Takeaway: drive phase reproduces LILAC within ±7% on every kinematic and thermodynamic metric. The deficit is in the burning phase — HS ρR collapses by 58% and yield falls 70% short. The drive calibration is fundamentally correct; something in the BURN physics is missing.
Mehlhorn → Trickey · Helios postprocess review · June 3 2026
4

## Slide 5
PART 1 · POLAR DIRECT DRIVE
Foam → ice isolation: foam EOS+opacity dominates the residual
Same fab007 geometry, drive, and pulse — only the main fuel layer changes:
Metric | Helios FOAM | Helios ICE | LILAC | 
Yield | 26 MJ | 81 MJ | 87 MJ | ice ≈ LILAC
Hot-spot ρR (T>4.5) | 0.35 g/cm² | 0.71 g/cm² | 0.85 g/cm² | ice → +103%
Burn-region ρ (g/cc) | 12 | 30 | (not reported) | ice 2.5× foam
What this rules in
Drive calibration is correct (ice → LILAC within 7%)
Wetted-foam main fuel is the dominant residual contributor
Foam burn-region density 60% below ice — burn rate ∝ n²⟨σv⟩ drops ~20× locally
What it does NOT prove (yet)
Whether foam deficit is a Helios algorithm bug or a real material-physics effect
Whether the PROPACEOS DT-CH foam EOS+opacity tables themselves are the limiting factor
Mehlhorn → Trickey · Helios postprocess review · June 3 2026
5

## Slide 6
PART 1 · POLAR DIRECT DRIVE
Three verification tests rule out Helios algorithm bugs
01
Bosch-Hale DT kernel
<0.4% error
Zero-D static plasma at n_DT=10²², T=3–15 keV. Helios FusionRate_DT_nHe4 vs analytic Bosch-Hale 1992 ⟨σv⟩. Pure DT AND 1.7%-C foam compositions.
Fusion kernel is exact within numerical tolerance.
02
NRL bremsstrahlung
within ḡ-factor
Same Zero-D setup. Helios brems-escape vs NRL P_brem = 1.69×10⁻³²·√T·n_e·Σ Z²n_Z. Pure DT: 2–5% offset (Karzas-Latter Gaunt vs NRL ḡ ≈ 1.11). Foam: expected Z-dependent C VI contribution.
Brems kernel correct; carbon arithmetic correct.
03
Planar laser ablation
decisive material test
Matched drive: 1×10¹⁴ W/cm², λ = 0.351 µm, 2 ns. DT slab vs DT-CH foam slab. PROPACEOS foam shows: −19% ablation pressure, −13% post-shock compression.
Material physics — not algorithm.
Conclusion: the foam-burn deficit vs LILAC is real PROPACEOS EOS+opacity material physics, not a Helios code bug.
Mehlhorn → Trickey · Helios postprocess review · June 3 2026
6

## Slide 7
PART 1 · POLAR DIRECT DRIVE
Ray-tracing geometry knobs — 1D limits, two paths to V_impl
Why 1D ray-trace can't reproduce 3D PDD
Helios spherical ray-trace maintains full coupling throughout the implosion
3D codes (HYDRA / LILAC / xRAGE) capture fixed-pointing NIF beams missing the shrinking capsule at late times
Helios systematically over-drives at late times by ~30–40% even at calibrated geometry
Hydro efficiency locks near 10–11% regardless of geometry — excess drive is in the ablation physics, not pure coupling
Two geometric paths to LILAC velocity — same residual
Config | PDD_26b | DM_01b
Cone half-angle | 20° (forward) | 3.5° (narrow)
Focus position d | +0.20 cm | −2.50 cm (inverted)
V_impl achieved | 478 km/s | 405 km/s
Adiabat (Lindl) | 1.43 | 1.56
Imploded DT mass | 0.60 mg | 0.60 mg
Same adiabat-and-mass residual across two very different beam geometries → ablation residual is downstream, not laser-coupling geometry.
Mehlhorn → Trickey · Helios postprocess review · June 3 2026
7

## Slide 8
PART 1 · POLAR DIRECT DRIVE
Design study: FL=0.012 + geometric defocus → two-plateau yield staircase
Chart: Yield vs cone angle (FL = 0.012, burn ON)
| 37° (baseline) | 33° | 28° | 25° | 20°
Yield (MJ) | 33 | 55 | 55 | 69 | 69
Plateau 1 · 55 MJ / 25% foam share
c33_burn — recommended (closest-to-LILAC anchor)
c28: foam over-compresses to 62 g/cc but burns NO more — bootstrap-limited
Plateau 2 · 69 MJ / 31% foam share
c25_burn — recommended (max-yield anchor)
Unlocks at spot 0.16→0.14, focus 0.18→0.16
c20 saturated and superseded by c25
LILAC reference: 87 MJ. Helios design study recovers 63–79% of LILAC yield with 25–31% foam-burn share (vs <15% at production FL=0.007).
Mehlhorn → Trickey · Helios postprocess review · June 3 2026
8

## Slide 9
PART 1 · POLAR DIRECT DRIVE
Foam burn is bootstrap-temperature-limited, not compression-limited
At bang time | fab02 (over-driven) | fab007 (calibrated) | 
Yield | 59 MJ | 26 MJ | over-driven yields more
Foam yield share | 26.5% | 10.1% | foam fires 2.6× more in fab02
Ice ⟨T_ion⟩ at bang | 34 keV | 17 keV | ice hot spot 2× hotter
Foam ⟨T_ion⟩ at bang | 4.4 keV | 1.85 keV | foam follows ice temperature
Foam zones crossing T > 4.5 keV | 68% | 21% | alpha-bootstrap reach into foam
Foam ρ_max at bang | 7.4 g/cc | 12.9 g/cc | fab007 foam DENSER — not the limit
PROPACEOS foam EOS is NOT broken
Foam reaches peak CR ≥ ice peak CR in both runs at compression times within 30–40 ps. Foam compresses fine. Hypothesis retired.
Foam burn ∝ alpha bootstrap STRENGTH
Foam fires in proportion to how strongly the ice hot spot ignites. fab02's 3.5× hotter ice bootstrap fires 68% of foam zones vs fab007's 21%.
Mehlhorn → Trickey · Helios postprocess review · June 3 2026
9

## Slide 10
PART 2 · HYBRID DIRECT DRIVE
HDD setup: WT_cthomas target → Thomas Vulcan reference
WT_cthomas target (Will Trickey's RHW)
Region | Zones | ρ₀ (g/cc)
DT gas | 0–25 | 6×10⁻⁴
DT/CD foam | 26–58 | 0.30
DT/CD foam_2 | 59–125 | 0.30
CD ablator | 126–155 | 1.09
CD ablator_2 | 156–189 | 1.09
Bisections (foam_2, CD_2) are diagnostic, not material changes. 189 total zones, 3-beam laser, 4.0 MJ delivered.
Thomas et al. Vulcan HDD reference
Yield | 256 ± 13 MJ
Target gain | 65 ± 3.3
V_impl | 410 ± 20 km/s
α_min at CR=1.5 | 6.00 ± 0.50
Hydro efficiency | 8.0 ± 0.4%
In-flight KE | 300 ± 15 kJ
Imploded DT mass | 3.0 ± 0.15 mg
Fraction absorbed | 97 ± 5%
⟨ρR_cf⟩ | 1.60 ± 0.08 g/cm²
Goal: reproduce Thomas reference + cross-validate against Will's RHINO postprocess.
Mehlhorn → Trickey · Helios postprocess review · June 3 2026
10

## Slide 11
PART 2 · HYBRID DIRECT DRIVE
Three calibration knobs identified — ranked by impact
K1
Bookkeeping
CD ablator EOS path resolution
±50% yield · NO kinematic effect
Original RHW references Windows path C:/Users/WilliamTrickey/…/CD.prp that doesn't resolve on Mac. Helios falls back silently to ideal-gas-like EOS. Same V_impl, same shock breakout, different bounce. With fallback: 196 MJ. With Studio-local CD table: 295 MJ.
K2
Secondary
Flux limiter (0.015 → 0.012)
regime-changing WITHOUT picket
+14% hydro eff (21.3 → 24.3); unablated fuel collapses from 75% to 0.7%; burn FWHM 82 ps → 6 ps (flash-burn). WITH picket applied, FL changes become second-order (±4% yield).
K3
Primary
Picket Trad modification
DOMINANT calibration lever
Creates 2-shock train (foot 7.88 + ramp 11.45 ns). Triples Lindl base adiabat (0.35 → 1.08). +14% on RHINO α_min (5.62 → 6.43). Drops over-driven hydro eff (24%) to Thomas-matched 8.3%.
Mehlhorn → Trickey · Helios postprocess review · June 3 2026
11

## Slide 12
PART 2 · HYBRID DIRECT DRIVE
Picket-vs-FL isolation: picket dominant, FL fine-tuning
Picket effect (FL held constant)
Comparison | Yield Δ | Hydro eff Δ | CR_max Δ | Burn FWHM
baseline_tm → picket_015 (FL=0.015) | 295 → 245 MJ (−17%) | 21.3 → 8.3% (−61%) | 113 → 53.7 (−52%) | 82 → 60 ps
baseline_012 → picket_012 (FL=0.012) | 303 → 256 MJ (−16%) | 24.3 → 8.3% (−66%) | 110 → 53.3 (−52%) | 6 → 65 ps (regime escape)
FL effect (picket held constant)
Comparison | Yield Δ | Hydro eff Δ | CR_max Δ | Burn FWHM
baseline_tm → baseline_012 (no picket) | 295 → 303 MJ (+3%) | 21.3 → 24.3% (+14%) | 113 → 110 (−3%) | 82 → 6 ps (regime change!)
picket_015 → picket_012 (picket on) | 245 → 256 MJ (+4%) | 8.3 → 8.3% (0%) | 53.7 → 53.3 (−1%) | 60 → 65 ps (+8%)
Recipe: establish picket first (primary lever; the 2-shock train is identical foot/ramp at 7.88/11.44–45 ns regardless of FL), then fine-tune FL within a small ±0.003 window. WITHOUT picket, FL changes are regime-determining (flash-burn vs assembly).
Mehlhorn → Trickey · Helios postprocess review · June 3 2026
12

## Slide 13
PART 2 · HYBRID DIRECT DRIVE
Production anchor: WT_cthomas_baseline_picket_012
Yield
256.4 MJ
vs 256 MJ
+0.1%
Hydro efficiency
8.3%
vs 8.0%
+4%
V_impl RHINO
389 km/s
vs 410 km/s
−5%
α_min RHINO
6.43
vs 6.00 ± 0.50
+7%
Secondary metrics — close to Thomas
In-flight KE | 258 vs 300 kJ | −14%
⟨ρR_cf⟩ | 1.17 vs 1.60 g/cm² | −27%
Assembled mass RHINO | 2.38 vs 3.0 mg | −21%
Foot / ramp shock | 7.88 / 11.45 ns (NEW) | 2-shock train
Persistent 1D residuals (same family as PDD fab007)
Fraction absorbed | 85% vs 97% | −12%
CR_max | 53.3 vs ~20 | +165%
⟨T_hs⟩ | 120 vs 47 keV | +157%
Imploded DT (core only) | 0.05 vs 3.0 mg | aperture artifact
Mehlhorn → Trickey · Helios postprocess review · June 3 2026
13

## Slide 14
PART 2 · HYBRID DIRECT DRIVE
RHINO cross-validation — same .exo, both pipelines
Direct postprocess of WT_cthomas_baseline.exo by Helios pipeline and Will's RHINO native:
Metric | Helios pipeline | RHINO native | Δ | Thomas published
Yield (MJ) | 196.2 | 196 | 0% | 256 ± 13
Laser absorbed (MJ) | 3.104 | 3.104 | 0% | —
V_impl RHINO (km/s) | 396.7 | 404.4 | −2% | 410 ± 20
Breakout time (ns) | 11.16 | 11.16 | 0% | —
t at CR=1.5 (ns) | 13.80 | 13.80 | 0% | —
Shell inner at CR=1.5 (cm) | 0.1224 | matches | <1% | —
α_min CR=1.5 (partially_ionized) | 5.62 | 4.125 | +36% | 6.00 ± 0.50
Reading agreement: yield, V_impl, breakout, t_cr15, shell geometry — both postprocessors read the .exo identically. Single disagreement (α_min) traced to ELECTRON-DENSITY CONVENTION (next slide).
Mehlhorn → Trickey · Helios postprocess review · June 3 2026
14

## Slide 15
PART 2 · HYBRID DIRECT DRIVE
Adiabat convention story — RESOLVED to 0.1%
Convention | n_e source | α_min on baseline.exo | Match
Our pipeline · partially_ionized | actual electron_density (per zone, EXODUS) | 5.62 | —
Our pipeline · fully_ionized_dt | n_e = ρ / m_avg_ion (assumes Z̄=1) | 4.13 | matches RHINO native → 0.1%
Will's RHINO native (default = fully_ionized_dt) | n_e = ρ / m_avg_ion | 4.125 | apples-to-apples ✓
Thomas published (HYDRA) | (see open question below) | 6.00 ± 0.50 | —
Mechanism
For pure DT zones (Z̄ = 1 at full ionization) the two conventions are identical. For multi-material DT/CD foam at partial ionization they diverge by the local Z̄ factor. Both conventions now available in pipeline: data.adiabat_min_rhino + data.adiabat_min_rhino_fully_ionized.
Open question for Cliff
Which n_e convention does HYDRA use for its reported α = 6.0? Most modern multi-physics codes track ionization per zone (= partially_ionized = our default = 5.62 on baseline, 6.43 on picket_012 → matches Thomas +7%). Will to confirm.
Mehlhorn → Trickey · Helios postprocess review · June 3 2026
15

## Slide 16
PART 3 · TOOLING
Pipeline improvements (June 2026)
RHINO conventions ported
Clean-room implementations of implosion_velocity (validated to ±2%) and min_shell_adiabat at CR=1.5 (validated to 0.1% in matching convention) from the RHINO source.
7 new RHINO diagnostics
max_shell_velocity_time, stagnation_time (RHINO convention), assembled_mass, burn_fraction, ablation_pressure_at_cr_3p5, shell_thickness + cr_inner histories, time_at_cr(cr) utility.
Convention-aware comparison framework
compare_with_published auto-routes each adiabat row to its convention-matching published JSON key (adiabat / adiabat_rhino_min_cr15 / adiabat_rhino_formula_*).
HDD design comparison plot
examples/hdd_design_comparison.py — 4-row + Thomas + RHINO reference figure for design-anchor selection.
RHINO 1.5.1 installed locally
~/Codes/RHINO on MacBook for direct same-.exo cross-checks. Used to validate the convention-resolution story.
EOS-loader fix
ion_density and mean_charge now loaded from EXODUS (needed for fully_ionized_dt adiabat). Both were standard EXODUS variables we'd been silently ignoring.
Mehlhorn → Trickey · Helios postprocess review · June 3 2026
16

## Slide 17
PART 3 · WHERE WE STAND
Calibration summary — three production anchors
Anchor | Knobs / configuration | Reference match | Verdict
Olson_PDD_20_fab007 (PDD production) | cone 37° / spot 0.18 cm / focus 0.22 cm / FL_prism 0.007 / foot 25 TW | LILAC kinematics + thermodynamic state to ±7%; yield 30% of LILAC | Drive calibration closed; foam burn deficit is real PROPACEOS physics
c33_burn / c25_burn (PDD design study) | FL_prism = 0.012 + geometric defocus (cone narrowing + spot/focus tightening) | c33: 55 MJ / 25% foam. c25: 69 MJ / 31% foam. vs LILAC 87 MJ / ~near parity | Recovers 63–79% of LILAC yield; foam burn productivity restored
WT_cthomas_baseline_picket_012 (HDD production) | FL = 0.012 + EOS-fixed CD ablator + picket Trad modification | Thomas reference ±7% on yield, hydro eff, V_impl, α_min RHINO | Production HDD anchor; structural metrics match
Persistent 1D residuals across both PDD and HDD: ⟨T_hs⟩ overshoot, fraction-absorbed deficit, CR_max over-compression. Same family on both targets — structural 1D-vs-3D physics gap, not calibration deficits closeable inside Helios 1D. (Assembled shell mass — the RHINO definition — matches Thomas to ~20% on HDD; the −98% “imploded mass” headline is a pipeline-aperture artifact, not a real deficit.)
Mehlhorn → Trickey · Helios postprocess review · June 3 2026
17

## Slide 18
PART 3 · LET'S TALK
Next steps for discussion
Tom → Cliff
n_e convention for Thomas α
Confirm whether HYDRA reports α with per-zone actual electron density (partially_ionized) or Z̄=1 assumption (fully_ionized_dt). Closes the convention story end-to-end.
Joint
RHINO stagnation_time definition
RHINO reports shell-velocity-min; our pipeline reports HS-radius-min (1.3 ns later). Decide whether to adopt RHINO's convention as the production default.
PDD
Re-extract historical anchors with RHINO-formula adiabat
fab007, fab02, c33_burn, c25_burn — generate parallel α values in both conventions for any future Xcimer cross-tool comparison.
HDD
Extend calibration to other Vulcan-class targets
Apply the picket-first recipe to additional Will-provided HDD geometries if available. Document calibration transfer pattern.
Tooling
pint-style units in high-risk code paths
Deferred for now (full discussion in earlier message). Pragmatic partial adoption recommended for adiabat / Fermi-pressure / burn-fraction calculations.
Docs
Production-anchor designation for Xcimer use
Formalize picket_012 + c33/c25 as the production calibration anchors for Xcimer reference. HDD report PDF/DOCX ready in docs/.
Mehlhorn → Trickey · Helios postprocess review · June 3 2026
18